## Slide 1
CODEALPHA
PHARMACEUTICAL RESEARCH INTERNSHIP
CASE STUDY – DRUG FORMULATION
Paracetamol 500 mg Immediate-Release Tablet
Formulation process • Excipients • Stability • Manufacturing challenges
500
500
500
Prepared by P. Tamilselvan
M.Pharm (Pharmaceutics)
CodeAlpha Pharmaceutical Research Internship • Task 2

## Slide 2
1. Product Profile & Formulation Objective
Case Study
Dosage form
Immediate-release oral tablet Representative 500 mg strength
Active pharmaceutical ingredient
Paracetamol (acetaminophen) Analgesic + antipyretic
Target product profile
Accurate dose • robust tablet Rapid disintegration • reproducible dissolution
Why this formulation is challenging
Paracetamol can present poor flow and compressibility, making powder handling and direct compression formulation more challenging.
The formulation must balance mechanical strength with rapid disintegration and dissolution.
Excipient selection and process control are therefore critical for content uniformity, tablet integrity and drug release.
Case-study approach
Representative academic formulation — exact commercial compositions vary by manufacturer.
Wet granulation is used here as the model manufacturing route.
Quality is assessed through physical, performance and stability attributes.
CodeAlpha Pharmaceutical Research Internship • Task 2

## Slide 3
2. Representative Formulation & Excipients
Formulation design
Component | Typical role | Why it is included
Paracetamol | API | Provides analgesic and antipyretic activity
Microcrystalline cellulose (MCC) | Diluent / compression aid | Improves bulk, compactibility and tablet formation
Povidone K30 | Binder | Promotes granule formation and cohesion
Croscarmellose sodium | Superdisintegrant | Promotes rapid tablet breakup after administration
Colloidal silicon dioxide | Glidant | Improves powder/granule flow
Magnesium stearate | Lubricant | Reduces friction during compression and ejection
Note: This is a representative formulation for an academic case study; excipient identity and quantity can differ across products and manufacturers.
CodeAlpha Pharmaceutical Research Internship • Task 2

## Slide 4
3. Manufacturing Process – Wet Granulation
Process flow
1
Dispensing & sieving
2
Dry mixing API + diluent
3
Binder solution addition
4
Wet massing & granulation
5
Drying & size control
6
Lubrication & blending
7
Compression into tablets
8
Coating / packing (if required)
Critical process controls: granule moisture • granule size • blend uniformity • compression force • tablet weight
CodeAlpha Pharmaceutical Research Internship • Task 2

## Slide 5
4. In-Process & Finished-Product Quality Checks
Quality control
Appearance
No visible defects; consistent dimensions/finish
Weight variation
Controls tablet-to-tablet mass consistency
Hardness & friability
Confirms mechanical strength and resistance to abrasion
Disintegration
Confirms prompt breakup for an immediate-release product
Dissolution
Assesses the rate/extent of drug release
Assay & content uniformity
Confirms identity, potency and dose consistency
A robust formulation should meet predefined specifications throughout manufacturing and shelf life.
CodeAlpha Pharmaceutical Research Internship • Task 2

## Slide 6
5. Stability Factors & Packaging
Stability
Temperature
Heat can accelerate chemical degradation and alter physical properties.
Moisture / humidity
Can influence degradation, granule/tablet properties and dissolution.
Light
Photostability should be considered where the API/formulation is light-sensitive.
Oxygen / oxidation
Oxidative stress can contribute to impurity formation.
Stability program
Monitor assay, degradation products, dissolution, appearance and relevant physical attributes over time.
ICH stability guidance evaluates how quality changes under environmental factors such as temperature, humidity and light.
Packaging should provide appropriate protection from moisture, light and handling conditions.
Packaging options
Blister pack or moisture-protective bottle
CodeAlpha Pharmaceutical Research Internship • Task 2

## Slide 7
6. Formulation & Manufacturing Challenges
Risk management
Poor flow / compressibility
May affect die filling and weight uniformity.
Granulation variability
Moisture and granule size can change compressibility and dissolution.
Sticking / picking
Can occur during compression and damage tablet surfaces.
Over-lubrication
Excessive lubricant mixing can reduce tablet strength or slow wetting/dissolution.
Content uniformity
API distribution must remain consistent across the batch.
Dissolution performance
Formulation and process changes can alter drug-release behavior.
Key principle: formulation development is an optimization exercise — improving one attribute can affect another.
CodeAlpha Pharmaceutical Research Internship • Task 2

## Slide 8
7. Conclusion & References
Take-home message
Conclusion
Paracetamol immediate-release tablets illustrate how API properties, excipient functionality and process design must work together.
Wet granulation can improve powder flow and compressibility, but it introduces additional process variables such as binder addition, drying and granule-size control.
Stability and quality evaluation should cover chemical integrity, physical performance and dissolution throughout the product lifecycle.
Selected references
1. EMA/ICH. ICH Q1A(R2): Stability Testing of New Drug Substances and Products.
2. FDA. Q1A(R2) Stability Testing of New Drug Substances and Products.
3. Arshady R. et al. Granulation techniques and technologies: recent progresses. Drug Design, Development and Therapy. 2015;9:4681–4696.
4. Study of formulation of pharmaceutical forms of paracetamol in medical practice. PubMed PMID: 21246913.
5. Todorović NB et al. Chemical Stability and Dissolution of Paracetamol Tablets Formulated by Direct Compression and Granulation Process. Acta Chim Slov. 2025; DOI: 10.17344/acsi.2025.9374.
Sources consulted: FDA • EMA/ICH • PubMed • peer-reviewed literature
Prepared by P. Tamilselvan | CodeAlpha Pharmaceutical Research Internship
CodeAlpha Pharmaceutical Research Internship • Task 2